MF Fire  - FireMAPS V.2 Installation Guide

MF Fire, Inc        FireMAPS V.2 Kit

Congratulations on being selected to Beta Test our latest Invention!!!

The FireMAPS V.2 kit in this box is a unique device that attached to your wood stove and gathers temperature readings in your flue and the position of your wood loading door. With this information, your MAPS device can process the local data and then send valuable guidance to your cellphone, so that you may adjust the door and bypass lever at exactly the proper time for the most efficient burn.

FireMAPS V.2 Components:

<<<<  Thermo-Couple Wire ( aka T.C. )

==============================================================

<<<<  I.R. Door Sensor & USB cable

==============================================================

<<<< FireMAPS AC Power Supply & Cord

Step #1  - Remove one screw from the Flue pipe at the

Collar and slowly insert the TC wire up to the bend.

Step #2  - Remove the one piece of Hi-Temp Tape ** from

the outside of the First Aid Kit and place it over the hole.

Step #3  - On the Lower Right side of your Stove

Attach the IR Door Sensor using the mangets.

Step #4  - Make sure it is postioned as shown

in the photo above and pushed back even with the door.

Step #5  - Attach the MAPS Box low in the back of the

Stove and plug the Power cord into an available AC Outlet.

** Please note: that you may smell the Hi-Temp tape during your

1st couple of burns, this is to be expected as the tape seals up.

Step #6 – Downloading the FireMAPS App and setting it up.   TBA